## Slide 1: Crowd Sourcing Water Turbidity Information
Nitay ozer
Itay mal
supervisor adi vainiger

## Slide 2: Project Goal
Low-cost, portable and highly available solution for crowdsourcing water turbidity information.
Based of personal smartphone, application and DIY measuring kit.

## Slide 3: Motivation
water quality
drinking/agriculture water sources
Environmental effects
Public health
Wildlife research
Sediment transport
Water Based Activities
Water sports
Diving

## Slide 4: What is turbidity
‘Fogginess’ of a fluid
Commonly measured by NTU or FTU
Image taken from: Hussain, I., Ahamad, K., & Nath, P. (2016). Water turbidity sensing using a smartphone. Rsc Advances, 6(27), 22374-22382.

## Slide 5: What is turbidity
Intense light scattering caused mainly by fine-particle sediment
Image: Davies-Colley, R.J. and Smith, D.G. (2001), TURBIDITY SUSPENDED SEDIMENT, AND WATER CLARITY: A REVIEW. JAWRA Journal of the American Water Resources Association, 37: 1085-1101.

## Slide 6: Absorption and Scattering
Tea has high absorption coefficient
Milk has high scattering coefficient

## Slide 7: Existing Solutions

## Slide 8: Nephelometer

## Slide 9: Nephelometer
The standard
Range of sizes
Based on light scattering
Advantages:
Most accurate
Disadvantages:
$$$

## Slide 10: Water turbidity sensing using a smartphone and attached device
Hussain, I., Ahamad, K., & Nath, P. (2016). Water turbidity sensing using a smartphone. Rsc Advances, 6(27), 22374-22382.

## Slide 11: Water turbidity sensing using a smartphone and attached device
Application + special device
Uses devices sensors and smartphone computing resources
Based on light scattering
Advantages:
Highly portable
High accuracy
Disadvantages:
Availability
$$

## Slide 12: ‘HydroColor: Water Quality App’

## Slide 13
Android smartphone application
Uses the smartphone's digital camera
Based on the reflectance of the water
Advantages:
Highly portable
Disadvantages:
Accuracy
$
calibration
‘HydroColor: Water Quality App’

## Slide 14: Possible Approaches

## Slide 15: Beam Attenuation
Light source is fixed
Camera moved horizontally
Measuring difference in backscattered light
Main Disadvantage:
  Requires external light to be negligible
  Requires “clean” scene

## Slide 16: Secchi Disk
Disk is lowered vertically
Measures by disappearance depth
Main disadvantage:
  Requires very deep water body

## Slide 17: Secchi Disk Improvements
Two targets – reduce required depth
Use color table target – specific wavelength

## Slide 18: Black Disk
Move the disk horizontally
Based on the disappearance distance
Main disadvantage:
  Requires very wide water body
  Additional complexity due to viewing apparatus

## Slide 19: Black Disk Improvements
Take photo underwater – reduce complexity and reflection effect
Two targets – reduce required distance

## Slide 20: Purposed Solution

## Slide 21: Basic Assumptions
Consistency of water turbidity in water body .
Invariant to light source.
Water body is big enough No reflectance from surroundings.
From the above:

## Slide 22: Measurement Setup

## Slide 23: Physical Model - Beer-Lambert Law
Where:

## Slide 24: Physical Model
Natural light

## Slide 25: Physical Model
From 1st target:
From 2nd target:

## Slide 26: Algorithm Description – Target Detection
Active Contours
Ellipse RANSAC
User Correction
1
2
3

## Slide 27: Algorithm Description – Target Distance Calculation
Calculated to each target separately according to:
Where:

## Slide 28: Algorithm Description – Targets Segmenting and Final Calculation
Thresholding the pixels contained in each target
Attenuation coefficients calculated in each color channel (RGB) by:

## Slide 29: Results

## Slide 30: Assumptions Validation
Environment Reflections

## Slide 31: Assumptions Validation
Light Hue and Radiance

## Slide 32: Assumptions Validation
Targets Distances

## Slide 33: Large Scale Testing
1331 simulation images
Near target distance
Far target distance = Near target distance + 0.6

## Slide 34: Large Scale Testing – Error Analysis
High Errors due to which is not physical
After outlier removal average error:

## Slide 35: Large Scale Testing – Error Analysis
Other possible error factors:
  Target localization error
  Mutual interference between targets (shadowing)
  Finite accuracy of pixel values
target 2
light source
target 1
shadow

## Slide 36: Application Demo

## Slide 37: Challenges

## Slide 38: Simulating Realistic Scene
Mitsuba 3 Readiness
Mitsuba 0.5 Properties Definition

## Slide 39: Target Detection Methods
Critical stage to the algorithm success
We have tried many approaches and variants
Chosen solution must be robust
Classical Approach (Hough)
Deep Learn Methods (DeepLab)

## Slide 40: Conclusions

## Slide 41: Conclusions
In this project we developed an affordable method for remote sensing of water attenuation properties that suits crowdsourcing.
The method has been proven as stable and accurate with physically based simulation products with ~4% error.
This project involves wide range of fields: computer vision and graphics, Image processing, ML, optics etc. we have learned a lot and gained valuable practical experience.
We hope that this project will be beneficial for future works and applications to come.

## Slide 42: Conclusions
Due to mentioned challenges, we failed reach some of our initial goals:
  Testing on real life images
  Converting attenuation coefficients to NTU/FTU
  Mobile device application development
  Web based database for result sharing

## Slide 43: Further Work Suggestions
Using color targets to isolate wavelength bands – profile contaminators.
Isolate scatter coefficient by measuring diffusion of pattern in targets.
Improving specific parts of our algorithm e.g. better automatic target detection.