## Slide 1: Crowd Sourcing Water Turbidity Information
Nitay ozer
Itay mal
supervisor adi vainiger

## Slide 2: Project Goal
Low-cost, portable and highly available solution for crowdsourcing water turbidity information.
Based of personal smartphone, application and DIY measuring kit.

## Slide 3: Motivation
water quality
drinking/agriculture water sources
Environmental effects
Public health
Wildlife research
Sediment transport
Water Based Activities
Water sports
Diving

## Slide 4: What is turbidity
‘Fogginess’ of a fluid
Commonly measured by NTU or FTU
Image taken from: Hussain, I., Ahamad, K., & Nath, P. (2016). Water turbidity sensing using a smartphone. Rsc Advances, 6(27), 22374-22382.

## Slide 5: What is turbidity
Intense light scattering caused mainly by fine-particle sediment
Image: Davies-Colley, R.J. and Smith, D.G. (2001), TURBIDITY SUSPENDED SEDIMENT, AND WATER CLARITY: A REVIEW. JAWRA Journal of the American Water Resources Association, 37: 1085-1101.

## Slide 6: Absorption and Scattering
Tea has high absorption coefficient
Milk has high scattering coefficient

## Slide 7: Existing Solutions

## Slide 8: Nephelometer

## Slide 9: Nephelometer
The standard
Range of sizes
Based on light scattering
Advantages:
Most accurate
Disadvantages:
$$$

## Slide 10: Water turbidity sensing using a smartphone and attached device
Hussain, I., Ahamad, K., & Nath, P. (2016). Water turbidity sensing using a smartphone. Rsc Advances, 6(27), 22374-22382.

## Slide 11: Water turbidity sensing using a smartphone and attached device
Application + special device
Uses devices sensors and smartphone computing resources
Based on light scattering
Advantages:
Highly portable
High accuracy
Disadvantages:
Availability
$$

## Slide 12: ‘HydroColor: Water Quality App’

## Slide 13
Android smartphone application
Uses the smartphone's digital camera
Based on the reflectance of the water
Advantages:
Highly portable
Disadvantages:
Accuracy
$
calibration
‘HydroColor: Water Quality App’

## Slide 14: Possible Approaches

## Slide 15: Beam Attenuation
Light source is fixed
Camera moved horizontally
Measuring difference in backscattered light
Main Disadvantage:
  Requires external light to be negligible
  Requires “clean” scene

## Slide 16: Secchi Disk
Disk is lowered vertically
Measures by disappearance depth
Main disadvantage:
  Requires very deep water body

## Slide 17: Secchi Disk Improvements
Two targets – reduce required depth
Use color table target – specific wavelength

## Slide 18: Black Disk
Move the disk horizontally
Based on the disappearance distance
Main disadvantage:
  Requires very wide water body
  Additional complexity due to viewing apparatus

## Slide 19: Black Disk Improvements
Take photo underwater – reduce complexity and reflection effect
Two targets – reduce required distance

## Slide 20: Purposed Solution

## Slide 21: Basic Assumptions
Water body dimension fit to measuring device
Turbidity conditions that fit for optical measurement
Daylight/mobile phone flashlight
Consistency of water turbidity in water body

## Slide 22: Measurement Setup

## Slide 23: Challenges in Simulating Realistic Scene
Sensor is inside the medium
Sensor is just outside the medium

## Slide 24: Simulations

## Slide 25: Block Diagram
Mobile Phone
Image pre-processing
Turbidity calculation
Raw image
Logger
Other smartphone sensors
Time, date, GPS location etc.
Web
Database
UI
Other user’s smartphones/computers
World wide measurements

## Slide 26: Milestones
so far:
Theoretical study
Chose optimal approach
Simulations
next:
Write and test the program
Mobile app
Targets kit

## Slide 27: Timeline
NOV
DEC
JAN
FEB
(EXAMS)
MAR
APR
MAY
Research
Algorithm
Development
APP
Measuring Kit
Adding Features
Simulations
Approach Selecting